## Slide 1: Chapter 8: Implementing Virtual Private Networks
CCNA Security v2.0
Daniel Valente
Fev 2016

## Slide 2: Chapter Outline
8.0 Introduction
8.1 VPNs
8.2 IPsec VPN Components and Operations
8.3 Implementing Site-to-Site IPsec VPNs with CLI
8.4 Summary

## Slide 3: Section 8.1: VPNs
Upon completion of this section, you should be able to:
Describe VPNs and their benefits.
Compare site-to-site and remote-access VPNs.

## Slide 4: Topic 8.1.1: VPN Overview

## Slide 5: Introducing VPNs
VPN Benefits:
Cost Savings
Security
Scalability
Compatibility
Notes: 8.1.1.1 Introducing VPNs

## Slide 6: Layer 3 IPsec VPNs
Notes: 8.1.1.2 Layer 3 IPsec VPNs

## Slide 7: Topic 8.1.2: VPN Technologies

## Slide 8: Two Types of VPNs
Remote-Access VPN
Site-to-Site VPN Access
Notes: 8.1.2.1 Two Types of VPNs

## Slide 9: Components of Remote-Access VPNs
Notes: 8.1.2.2 Components of Remote-Access VPNs

## Slide 10: Components of Site-to-Site VPNs
Notes: 8.1.2.3 Components of Site-to-Site VPNs
8.1.2.4 Activity – Compare Remote-Access and Site-to-Site VPNs

## Slide 11: Section 8.2: IPsec VPN Components and Operation
Upon completion of this section, you should be able to:
Describe the IPsec protocol and its basic functions.
Compare AH and ESP protocols.
Describe the IKE protocol.

## Slide 12: Topic 8.2.1: Introducing IPsec

## Slide 13: IPsec Technologies
IPsec Implementation Examples
IPsec Framework
Notes: 8.2.1.1 IPsec Technologies

## Slide 14: Confidentiality
Confidentiality with Encryption:
Notes: 8.2.1.2 Confidentiality

## Slide 15: Confidentiality (Cont.)
Encryption Algorithms:
Notes: 8.2.1.2 Confidentiality (Cont.)

## Slide 16: Integrity
Hash Algorithms
Security of Hash Algorithms
Notes: 8.2.1.3 Integrity

## Slide 17: Authentication
Peer Authentication Methods
PSK
Notes: 8.2.1.4 Authentication

## Slide 18: Authentication (Cont.)
RSA
Notes: 8.2.1.4 Authentication (Cont.)

## Slide 19: Secure Key Exchange
Diffie-Hellman Key Exchange
Notes: http://www.watchguard.com/help/docs/wsm/xtm_11/en-US/index.html#cshid=en-US/bovpn/manual/diffie_hellman_c.html
Diffie-Hellman (DH) groups determine the strength of the key used in the key exchange process. Higher group numbers are more secure, but require additional time to compute the key.
DH Group 1: 768-bit group
DH Group 2: 1024-bit group
DH Group 5: 1536-bit group

## Slide 20: Topic 8.2.2: IPsec Protocols

## Slide 21: IPsec Protocol Overview
Notes: 8.2.2.1 IPsec Protocol Overview

## Slide 22: Authentication Header
AH Protocols
Notes: 8.2.2.2 Authentication Header

## Slide 23: Authentication Header (Cont.)
Router Creates Hash and Transmits to Peer
Peer Router Compares Recomputed Hash to Received Hash
Notes: 8.2.2.2 Authentication Header (Cont.)

## Slide 24: ESP (Encapsulation Security Payload)
Notes: 8.2.2.3 ESP

## Slide 25: ESP Encrypts and Authenticates
Notes: 8.2.2.4 ESP Encrypts and Authenticates

## Slide 26: Transport and Tunnel Modes
Apply ESP and AH in Two Modes
Notes: Transport mode provides the protection of our data, also known as IP Payload, and consists of TCP/UDP header + Data, through an AH or ESP header. The payload is encapsulated by the IPSec headers and trailers. The original IP headers remain intact, except that the IP protocol field is changed to ESP (50) or AH (51), and the original protocol value is saved in the IPsec trailer to be restored when the packet is decrypted.
IPSec transport mode is usually used when another tunneling protocol (like GRE) is used to first encapsulate the IP data packet, then IPSec is used to protect the GRE tunnel packets. IPSec protects the GRE tunnel traffic in transport mode.

## Slide 27: Transport and Tunnel Modes (Cont.)
ESP Tunnel Mode
Notes: 8.2.2.5 Transport and Tunnel Modes (Cont.)
8.2.2.6 Activity – Compare AH and ESP

## Slide 28: Topic 8.2.3: Internet Key Exchange

## Slide 29: The IKE Protocol
Notes: 8.2.3.1 The IKE Protocol

## Slide 30: Phase 1 and 2 Key Negotiation
Notes: ISAKMP - Internet Security Association and Key Management Protocol

## Slide 31: Phase 2: Negotiating SAs
Notes: 8.2.3.3 Phase 2: Negotiating Sas
8.2.3.4 Video Tutorial – IKE Phase 1 and Phase 2

## Slide 32: Section 8.3: Implementing Site-to-Site IPsec VPNs with CLI
Upon completion of this section, you should be able to:
Describe IPsec negotiation and the five steps of IPsec configuration.
Configure the ISAKMP policy.
Configure the IPsec policy.
Configure and apply a crypto map.
Verify the IPsec VPN.

## Slide 33: Topic 8.3.1: Configuring a Site-to-Site IPsec VPN

## Slide 34: IPsec Negotiation
IPsec VPN Negotiation: Step 2 - R1 and R2 negotiate an IKE Phase 1 session.
IPsec VPN Negotiation: Step 1 - Host A sends interesting traffic to Host B.
IPsec VPN Negotiation: Step 3 - R1 and R2 negotiate an IKE Phase 2 session.
Notes: 8.3.1.1 IPsec Negotiation

## Slide 35: IPsec Negotiation (Cont.)
IPsec VPN Negotiation: Step 4 - Information is exchanged via IPsec tunnel.
IPsec VPN Negotiation: Step 5 - The IPsec tunnel is terminated.
Notes: 8.3.1.1 IPsec Negotiation (Cont.)

## Slide 36: Site-to-Site IPsec VPN Topology
Notes: 8.3.1.2 Site-to-Site IPsec VPN Topology

## Slide 37: IPsec VPN Configuration Tasks
XYZCORP Security Policy | Configuration Tasks
Encrypt traffic with AES 256 and SHA | 1. Configure the ISAKMP policy for IKE Phase 1
Authentication with PSK | 2. Configure the IPsec policy for IKE Phase 2
Exchange keys with group 24 | 3. Configure the crypto map for IPsec policy
ISAKMP tunnel lifetime is 1 hour | 4. Apply the IPsec policy
IPsec tunnel uses ESP with a 15-min. lifetime | 5. Verify the IPsec tunnel is operational
Notes: 8.3.1.3 IPsec VPN Configuration Tasks

## Slide 38: Existing ACL Configurations
ACL Syntax for IPsec Traffic
Notes: 8.3.1.4 Existing ACL Configurations

## Slide 39: Existing ACL Configurations (Cont.)
Permitting Traffic for IPsec Negotiations
Notes: 8.3.1.4 Existing ACL Configurations (Cont.)

## Slide 40: Introduction to GRE Tunnels
Notes: 8.3.1.5 Introduction to GRE Tunnels
8.3.1.6 Activity – Order the IPsec Negotiation Steps

## Slide 41: Topic 8.3.2: ISAKMP Policy

## Slide 42: The Default ISAKMP Policies
Notes: 8.3.2.1 The Default ISAKMP Policies

## Slide 43: Syntax to Configure a New ISAKMP Policy
Notes: 8.3.2.2 Syntax to Configure a New ISAKMP Policy

## Slide 44: XYZCORP ISAKMP Policy Configuration
Notes: 8.3.2.3 XYZCORP ISAKMP Policy Configuration

## Slide 45: Configuring a Pre-Shared Key
The crypto isakmp key Command
Notes: 8.3.2.4 Configuring a Pre-Shared Key

## Slide 46: Configuring a Pre-Shared Key (Cont.)
Pre-Shared Key Configuration
Notes: 8.3.2.4 Configuring a Pre-shared Key (Cont.)

## Slide 47: Topic 8.3.3: IPsec Policy

## Slide 48: Define Interesting Traffic
The IKE Phase 1 Tunnel Does Not Exist Yet
Notes: 8.3.3.1 Define Interesting Traffic

## Slide 49: Define Interesting Traffic (Cont.)
Configure an ACL to Define Interesting Traffic
Notes: 8.3.3.1 Define Interesting Traffic (Cont.)

## Slide 50: Configure IPsec Transform Set
The crypto ipsec transform-set Command
Notes: 8.3.3.2 Configure IPsec Transform Set

## Slide 51: Configure IPsec Transform Set (Cont.)
The crypto ipsec transform-set Command
Notes: 8.3.3.2 Configure IPsec Transform Set (Cont.)

## Slide 52: Topic 8.3.4: Crypto Map

## Slide 53: Syntax to Configure a Crypto Map
Notes: 8.3.4.1 Syntax to Configure a Crypto Map

## Slide 54: Syntax to Configure a Crypto Map (Cont.)
Crypto Map Configuration Commands
Notes: 8.3.4.1 Syntax to Configure a Crypto Map (Cont.)

## Slide 55: XYZCORP Crypto Map Configuration
Crypto Map Configuration:
Notes: 8.3.4.2 XYZCORP Crypto Map Configuration

## Slide 56: XYZCORP Crypto Map Configuration (Cont.)
Crypto Map Configuration:
Notes: 8.3.4.2 XYZCORP Crypto Map Configuration (Cont.)

## Slide 57: Apply the Crypto Map
Notes: 8.3.4.3 Apply the Crypto Map

## Slide 58: Topic 8.3.5: IPsec VPN

## Slide 59: Send Interesting Traffic
Use Extended Ping to Send Interesting Traffic
Notes: 8.3.5.1 Send Interesting Traffic
8.3.5.2 Verify ISAKMP and IPsec Tunnels

## Slide 60: Verify ISAKMP and IPsec Tunnels
Verify the ISAKMP Tunnel is Established
Notes: 8.3.5.2 Verify ISAKMP and IPsec Tunnels

## Slide 61: Verify ISAKMP and IPsec Tunnels (Cont.)
Verify the IPsec Tunnel is Established
Notes: 8.3.5.2 Verify ISAKMP and IPsec Tunnels (Cont.)

## Slide 62: Section 8.4: Summary
Chapter Objectives:
Explain the purpose of VPNs.
Explain how IPsec VPNs operate.
Configure a site-to-site IPsec VPN, with pre-shared key authentication, using the CLI.
Notes: 8.4.1.1 Video Demonstration – Site-to-Site IPsec VPN Configuration
8.4.1.2 Packet Tracer – Configure and Verify a Site-to-Site IPsec VPN
8.4.1.3 Lab – Configuring a Site-to-Site VPN
8.4.1.4 Chapter 8: Implementing Virtual Private Networks